## Slide 1: ARM Based SoC Verification
Presenter Name

## Slide 2: Agenda
ARM Based SoC Architecture
UVM TB Design
Bringup and CPU Boot
Fabric Verification
PCR Verification
Boot Flow
GLS/DFX Verification

## Slide 3: ARM Based SoC Architecture

## Slide 4: ARM Based SoC Architecture
A-Class Based Cluster
M-Class Based Subsystem for Security/PCR Management
Fabric
  Coherent Interconnect
    CCI/CMN
  Non-Coherent Interconnect
    NI-Tower
  GIC Interrupt controller
  LSIO
Subsystems
  LPDDR Subsystems
  HSIO Subsystem
Debug CSS600 Components

## Slide 5: ARM Based SoC Architecture
A-Class Based Cluster (ARMv8/v9 Architecture)
  Big Core
  Medium Core
  Little Core
M-Class Based Subsystem for Security/PCR Management
  M85/M55 Core
  AON subsystem
  Powering up Interconnect/PLLs
  Init Subsystems
Fabric
  Interconnects/Memory map
  GIC/Interrupt map

## Slide 6: ARM Based SoC Architecture
Debug
  APB ROM Table for Discovery
  AHBAP/AXIAP Memory View
  AP/DP Ports
  CTI
  Trace
Security
  Secure Transactions using CPU MMU Tables, IO Masters SMMU page tables
  RME features
  Debug Security
    SPIDEN/NIDEN
Boot
  M-Class Authentication using OTP

## Slide 7: ARM Based SoC : UVM Testbench Design
Clock/Reset Agents
P/Q Channel Agents
CHI Agents
ACE Agents
Memory responders
MailBox
Test End Mechanism
Coverage/Scoreboard

## Slide 8: ARM Based SoC : C + UVM Testbench Design
ASM Code for A/M Class processor
ARM RVDS compiler
Scatter file to generate hex code
Preload of hex code
Reset/Clock to CPU RTL using UVM TB
CPU Executing Boot Code and C-Test as
Test End mechanism (C + UVM Drop objections)

## Slide 9: ARM Based SoC : C + UVM Testbench Design
SoC Bringup and C-Testcase execution
  ASM Code
    boot.s
      Init general purpose registers (x0-x30, r0-r12)
      Init stack pointer and vector table
      system_init()
      jump to __main
        Internally Jumps to main()
    vect.s
      Vector table
    Page Tables for A-Class Processor
  C-Code
    All Drivers (GIC/SMMU/PL011/DDR … )
    Memory map definition mem_map.h
    Interrupt map definition intr_map.h
armclag to compile .asm files
armclag to compile .c files
armlink to link .o files using scatter load
elf2hex converter to get hex files
readmemh to preload the files

## Slide 10: ARM Based SoC : C + UVM Testbench Design
Reset Handler (ASM Code)
Identification of Core
System_init
main()
test_end()
run_phase clock/reset sequences
Event/mail_box wait
event to trigger sequences
Coverage/scoreboarding
drop_objections

## Slide 11: ARM Based SoC : Bringup and CPU Boot
Preload hex code in reset vector pointed memory
2. Core starts executing after reset / clock
Enable tarmac for debugs
CPU Powers up and executes bootcode + simple hello_world test, write to LSIO UART and prints

## Slide 12: ARM Based SoC : Software Library
Software Boot code Library availability for A/M/R Cores
2. Software interrupt handling for A+M class processors
Memory read/write functions
Power C-Library
Drivers for LSIO and Peripherals
Deep knowledge on both GCC and ARM compiler

## Slide 13: ARM Based SoC : Fabric Verification
Memory map verification using UVM Agents
2. Interrupt map, connectivity + functional verification
3. Debug discovery
4. IOPAD
5. Fuse

## Slide 14: ARM Based SoC : PCR Verification
Clock domain verification
  Clock gating/ungating
  All clock q-channel q-active contributor checks
2. Power Verification
  Functional verification scenarios
  Power domain ON->OFF/FUNC/FULL_RET->WARM_RESET
3. Power Verification : UPF
  PST verification
  Clamp assertions
  QPA Assertions
  Clock gating + Power scenarios

## Slide 15: ARM Based SoC : Boot Flow
Verification of Boot Flow Specific to the SOC
Running Software BootFlow on RTL

## Slide 16: ARM Based SoC : GLS Verification
Zero Delay
  NRF
  LEC Clean DFT Inserted netlist
  TB Updates due to bit-blasted flattened netlist
  X-prop debugs
BISR
  Memory repairs

## Slide 17: Thank you